## Slide 1: Selecting, Cutting, and Shaping Wood
Unit 9
Pages 101-118

## Slide 2: Characteristics of Wood and Lumber
Wood:
    The hard, compact fibrous material that comes from the branches and stems of trees.
Annual Rings:
    Patterns caused by hardening of the xylem and phloem of a plant, as new xylem and phloem are developed each year. Responsible for the appearance of the wood grain.
Species:
    Plants or animals with the same characteristics. Crucial in the selection of wood, some are better for decoration, some resist rot, some are hard, some are softer.

## Slide 3: How a Tree Grows

## Slide 4: Hardwood vs. Softwood
Softwood:
    Lumber that is derived from coniferous or evergreen trees. (trees that keep their leaves through winter)
      Pine, Douglas Fir, Redwood
Hardwood
    Lumber that is derived from deciduous trees. (loose their leaves in the fall and winter)
      Oak, Maple, Cherry, Walnut

## Slide 5: Lumber Grades
Hardwood Grades:
  Usable, clear Lumber in a board
      Clear = free of knots
        Knots = where branches attach to the tree.
  Highest Grade
    FAS – First and Seconds
      8’ long
      6” wide
      83% clear

## Slide 6: Lumber Grades
FAS-1
    Only one side of the board meets FAS
FAS and FAS-1 are used for very fine woodworking.

## Slide 7: Average Hardwood Grades
Number 1 Common
  1C = 4’ long, 3” wide, 67% clear
Number 2 Common
  2C = 4’ long, 3” wide, 50% clear
Number 3 Common
  3AC = 4’ long, 3” wide, 33% clear

## Slide 8: Softwood Grades
Yard Lumber
  3 Grades
    Select, Common, and Dimension
  Select: used where appearance is important, fascia boards, trim, etc…
    Defects can be covered by paint or finish
    Further divided into Grade A, B, C, & D Select

## Slide 9: Softwood Grades
Common
  Used in construction where appearance is not important.
    Further divided into Number 1,2,3,4,5 Common.
    Number 5 Common is the lowest quality lumber available.

## Slide 10: Softwood Grades
Dimension
  Used where strength is needed
    Rafters, studs, joists, etc…
      Graded based on
        Straightness
        Rigidity
        Strength
    Further graded into number 1, 2, 3 Dimension, depending upon use.

## Slide 11: Achieving Quality Lumber
Sawing Method
  Plain Sawn
    Cut parallel to the grain
    Grain appears wide
    Most common method for sawing
  Quartersawn
    Log is divided into quarters
    Each quarter is sawn separately
    Results in less distortion

## Slide 12
Plain-sawed or Plain sawn Lumber

## Slide 13: Quartersawn Lumber

## Slide 14: Curing Lumber
Trees are harvested Alive
Xylem and Phloem contain Water
  Green Lumber 120-130% moisture content
Lumber must be dried
Construction Lumber must be 15% or less moisture
Lumber shrinks and distorts as it dries.
Interior lumber must be 6-8% moisture.
Air drying is timely
  Up to 1 year per inch of thickness
After air drying wood can be kiln dried to 6-8%.
  Kiln is a large oven that slowly heats the wood removing excess moisture.

## Slide 15: Lumber Finish
Lumber is sold in 4 standard finishes
  Rough
    Not planed
    Not sized
    Straight from the sawmill
  S2S surfaced two sides
    Same thickness
    Varying width
    Rough edges

## Slide 16: Lumber Finish
S4S surfaced four sides
  The sides and edges are planed to exact dimensions.
Sanded
  Dimensions are exact
  All surfaces are sanded

## Slide 17: Standard Lumber Sizes
Boards direct from the sawmill are rough cut.
  Not to an exact dimension
    2x4 may be 2¼ x 4 ¼
    Boards are finished at the lumber mill
    Finished boards are also not the size they say they are, or nominal size
    A S4S 2x4 is actually 1½” x 3½”

## Slide 18: Cutting Lumber
Several types of saws are available
  Handsaws and mechanical saws
  Basic handsaws
    Crosscut saws
      Used for cutting across the grain
      Making boards shorter
    Rip Saw
      Used for cutting along the width of the board or with the grain.
      Making boards narrower.

## Slide 19: Cutting Lumber

## Slide 20: Cutting Lumber

## Slide 21: The Kerf
Cutting boards removes part of the board.
This is where sawdust comes from
We must account for this kerf when we are laying out our projects.
Typically saw blades will leave a 1/8” Kerf.

## Slide 22: The Kerf

## Slide 23: Dados and Rabbets
Not all cuts we make will go through an entire board.
  Dados and rabbets are cuts or grooves made to receive another board to make a stronger joint.

## Slide 24: Dados and Rabbets
Rabbets are used on end joints like drawer corners.