## Slide 1: Fastening Wood
Unit 10
Pages 119-127

## Slide 2: Wood Joints
A union of two pieces
  Several types
    Butt, Lap, Dado, Miter, Dovetail
  Type based on desired strength and appearance
  Several ways to secure a joint
    Nails, Screws, glue, or bolts

## Slide 3: Types of Wood Joints
Butt Joint
  Two pieces joined end to end
  Or edge to edge
  In line or at 90°
  Fairly weak
  Strengthened by wood or metal plates across the joints.

## Slide 4: Types of Wood Joints
Lap Joint
  Two pieces joined face to face
  In line or at 90°
  Stronger than butt joints

## Slide 5: Types of Wood Joints
Dado Joint
  Rectangular groove in one board that receives the end of another member
  Found in body of board not end
  Can be held with only glue if fit up is good.

## Slide 6: Types of Wood Joints
Rabbet Joint
  No bunny ears here
  Dado at the end of a board
  Common in cabinet and box making
  Squares easily if cut correctly

## Slide 7: Types of Wood Joints
Miter Joints
  Two ends cut to 45°
  Fits up to perfect 90°
  Common in finish trim and frames
  Can be secured with glue only
  Used on Nail-box project

## Slide 8: Types of Wood Joints
Dovetail Joints
  Interlocking fingers and grooves
  One of the strongest joints
  Used in fine furniture
  Secured by glue only

## Slide 9: Types of Wood Joints
Mortise and Tenon
  One of the oldest joints in woodworking
  Very strong
  Can be glued, pinned, or wedged

## Slide 10: Types of Wood Joints
Dowels
  Method of strengthening joints
  Round pegs of wood
    Typically sold in 36” lengths and cut to size
    Can be purchased in various diameters and lengths
  Insert into complimentary holes in pieces
  Similar to mortise and tenon

## Slide 11: Types of Joints
Biscuit Joints
  are thin ovals of manufactured wood.
  Slots are cut with a biscuit tool in the complimentary boards
  Glue is used to secure
  Clamps required until dry
  Fairly new
  Similar to dowels

## Slide 12: Fastening with Nails
Fastest way to secure wood
Very weak
Least rigid of all fastening options
Several types of nails
  Box, Common, finish, roofing, etc…
Typically driven with a hammer
  Pneumatic and electric nail guns make nailing much easier on carpenter

## Slide 13: Fastening with Nails
Selecting a hammer
  Hammers have different weights
    Typically 7, 13, 16, and 20 ounce
    The heavier the hammer can drive larger nails
Selecting Nails
  Nail size and type are determined by application
  Nails are sized by pennies
    Derived from British, how many pennies it took to buy 100 nails of a given size. The smaller the penny the smaller the nail
  A lower case d represents the penny weight.
  2d is about 1”, a 60d is about 6”

## Slide 14: Fastening with Nails
Nails may be pulled with a claw hammer.
  Leverage is the key
  Use a scrap block to add leverage and protect work.
  See figure 10-4 page 120

## Slide 15: Fastening with Nails
Types of nailing
  Toe Nailing
    Nails driven at 45°
    Fastening 2 boards at 90° one end to a face
  End Nailing
    Nails driven through the thickness of one board into the end of another
    Nail parallel to end piece grain
    Very weak

## Slide 16: Fastening with Nails
Flat Nailing
  Two flat pieces nailed together
  Thick to thin
  Thin to thin may require clinching
    Bending nail at 90°
    If splitting occurs clinch across the grain
    Clinching is very strong way to nail.

## Slide 17: Fastening with Nails
Setting Nails
  Finish carpentry requires nails to be hidden
  Setting nails achieves this
  Finish nails are driven below the surface of the wood to be covered
  Accomplished with a nail set
    Punch like tool with a cupped end to stay on nail head
    Nails should be set to at least 1/16”

## Slide 18: Fastening with Screws
Screws are stronger than nails
Several head types
Threads bite into wood for secure hold
core

## Slide 19: Countersinking
Drilling pilot, shank hole and countersink
Conceals the screw.
Countersink Bit
Pilot
Shank
Countersink

## Slide 20: Fastening with Bolts
Bolts differ from screws in thread type
  Require washers and nuts
  Can be the strongest way to fasten wood
  Holes drilled for bolts equal the diameter of the bolt.
  Carriage bolts often used
    Square shank prevents
    bolt from spinning.

## Slide 21: Fastening with Glue
Extremely Strong
  Stronger than nails
  As strong as the wood or stronger
Chemical Bond
Several types
  Resorcinol, urea, polyvinyl, epoxy, contact cement, casein, and animal glues
Most common wood glue is
  Aliphatic resin, or carpenter’s glue

## Slide 22: Fastening with Glue
Joints to be glued must be properly prepared.
  No paint, grease, or wax
  Sand the joint to ensure wood to wood contact.
  Glue is used solo, or with nails, screws and bolts.
Glued joints must be clamped until glue sets
We will glue all immovable wood joints